The colored ink stamp indicates this is a controlled document. Absence of color indicates this copy is not controlled and will not receive revision updates.

# Purpose

If sample results are not duplicating well, an outlier test may need to be performed in order to determine if specific results can be excluded from consideration.  An outlier test may be required on other sets of data, such as method qualification or method validation.  The Office of the Texas State Chemist uses the Dixon outlier test with critical values, at 5% error, as listed in the Use of Statistics to Develop and Evaluate Analytical Methods by Grant T. Wernimont, edited by William Spendley.

# Scope / Field of Application

The Dixon outlier test is to be used whenever the analytical results fail the duplication requirements a second time.  It can also be used when completing validation and/or training studies.

# Responsibilities

Chemists and others performing outlier evaluation – follow the SOP and complete all outlier procedures

Laboratory Director and Manager, Quality Assurance – monitor and ensure procedure is followed and documented

# Procedure

DIXON TEST AS APPLIED TO ANALYTICAL RESULTS

For a problem sample which fails the duplication requirement, it may be necessary to determine if a particular analytical result is an outlier.  Perform the following steps to make this determination.

List the four results in order of increasing magnitude (W, X, Y, Z).

Calculate the range (R) of the values (highest-lowest) (Z - W)

Determine which result is the suspected outlier (W or Z).

Calculate the difference (T) between the suspected outlier and its nearest neighbor:

If W is suspect: Tw = X - W

If Z is suspect:   Tz = Z - Y

Calculate the ratio (I):

If W is suspect:  I = Tw / R

If Z is suspect:   I = Tz / R

If I is greater than or equal to the critical value of 0.829 (for N = 4), then the suspect number is an outlier and can be excluded from consideration.  If I is less than 0.829, then the suspect number is NOT an outlier and should be kept in consideration.  Typically, the average of all non-outlier results will be reported out.

DIXON TEST AS APPLIED TO OTHER SITUATIONS

The same principle above can be applied to numeric data where N is other than 4.  Table 1 displays the critical values for N between 3 and 40.  NOTE: Use a different calculation for N > 8 (see references).

If a data set is greater than 40, split the data randomly in half and test for outliers at either end of the range of results.

Use the outlier spreadsheet for determining outliers in qualification sets.

TABLE 1

| N | Critical Value | N | Critical Value |
| --- | --- | --- | --- |
| 3 | 0.970 | 22 | 0.468 |
| 4 | 0.829 | 23 | 0.459 |
| 5 | 0.710 | 24 | 0.451 |
| 6 | 0.628 | 25 | 0.443 |
| 7 | 0.569 | 26 | 0.436 |
| 8 | 0.608 | 27 | 0.429 |
| 9 | 0.564 | 28 | 0.423 |
| 10 | 0.530 | 29 | 0.417 |
| 11 | 0.502 | 30 | 0.412 |
| 12 | 0.479 | 31 | 0.407 |
| 13 | 0.611 | 32 | 0.402 |
| 14 | 0.586 | 33 | 0.397 |
| 15 | 0.565 | 34 | 0.393 |
| 16 | 0.546 | 35 | 0.388 |
| 17 | 0.529 | 36 | 0.384 |
| 18 | 0.514 | 7 | 0.381 |
| 19 | 0.501 | 38 | 0.377 |
| 20 | 0.489 | 39 | 0.374 |
| 21 | 0.478 | 40 | 0.371 |

# References

Davis, F.A., Maxfield, M. W., Statistical Manual,  Dover Publications, NY, 1960.

Dixon W. J., Processing Data for Outliers, Biometrics, March 1953, pgs 74-89.

International Organization for Standardization (ISO) document ISO5725-1981.

Spendley, W. (ed.), Use of Statistics to Develop and Evaluate Analytical Methods, AOAC, 1985, Arlington, VA.  Table A-9, p. 156.

# Revision History

.